## Slide 1: Performance Analysis of Renderscript - Prakalp Srivastava, Cuong Manh Pham, and Abdul Dakkak

## Slide 2: Programmability of Heterogeneous Systems
Modern smartphone SoC
Main Memory
Interconnect
Modem
GPS
DSP
DSP
GPU
A/V Hardware Accelerators
DSP
Multi-media
CPU
L1 Cache
L2 Cache
CPU
L1 Cache
Vector
Vector
7 different parallelism models
Incompatible memory systems
6 different hardware ISAs
Need easier programmability!

## Slide 3: Today’s Solutions
OpenMP
CUDA
OpenCL
RenderScript
  Target at computationally intensive and data-parallel tasks
  Focus on: Portability and Development Efficiency
  Scheduling at runtime: parallelize work across all available computing resources, such as CPUs, GPUs, and DSPs
  Mobile centrics

## Slide 4: Mobile vs. Desktop
Requirements
  Power is as important as performance on mobile
  Ease of development and deployment
Users
  Might use compute intensive applications without knowing it
Distribution
  Cannot depend on non-native libraries
  No concept of package dependencies

## Slide 5: Desktop Heterogeneity
Practically every desktop is x86 machine with either an Intel, ATI, or NVIDIA GPU
Homogenous hardware
Heterogeneous software
Thousands of programming languages

## Slide 6: Mobile Heterogeneity
Practically every mobile is running either IOS or Android
Heterogeneous hardware
Homogenous software
Few programming languages

## Slide 7: RenderScript’s Approach

## Slide 8: RenderScript Offline Compilation
foo.rs
Offline Compiler
foo.bc
ScriptC_foo.java
ScriptField_s.java
...
LLVM Codegen
Java Wrapper Files
Bundled with final application file
Compiled with rest of application *.java files

## Slide 9: RenderScript Online JIT Compiler Flow
foo.bc
ScriptC_foo.java
ScriptField_s.java
...
App Java Source Files
Online JIT Compiler
Java VM JIT
Final Application File
ARM Cores
Accelerators (GPUs, DSPs)
...

## Slide 10: RenderScript Example

## Slide 11: RenderScript Example contd.

## Slide 12: RenderScript Claims
Offline Compiler
Embeds information in bitcode
Online JIT Compiler
Performs target-specific optimizations and code generation
  Using information embedded in bitcode
We need comprehensive performance analysis to test their claim
But
HW-specific features are deliberately not exposed for portability

## Slide 13: Methodology
Performance analysis of compute kernels
  Measure the compute time against both the optimized and unoptimized OpenCL implementations
  Measure the compute time against the threaded C version using Android’s NDK

## Slide 14: Methodology
Power analysis of benchmarks
  User Androids performance metrics to measure power usage
  Compare the power draw against OpenCL and the native multithreaded implementations

## Slide 15: Methodology
Programmability (objectively measured)
  How does RenderScript compare with OpenCL in terms of programmability?
  Does hiding architectural details, while adding runtime and compiler optimizations, result in performance close to hand tuned kernels?
  Are there any missed optimizations from the RenderScript compiler and/or runtime?
  Are there any RenderScript compiler optimizations that would benefit OpenCL or CUDA programmers.

## Slide 16: Related Work: OpenCL
OpenCL vs. CUDA: extensively studied. Consensuses:
  CUDA is generally better on NVIDIA GPUs
  OpenCL has sufficient interface to provide arch. details
    Peak performance comparable with CUDA
    Performance portability
  Compilers matter
Source image: K. Komatsu, K. Sato, Y. Arai, K. Koyama, H. Takizawa, and H. Kobayashi. Evaluating performance and portability of opencl programs. In The fifth international workshop on automatic performance tuning, 2010.
Tested on NVIDIA
Tesla C1060
Notes: NVIDIA
Tesla C1060 (Tesla)

## Slide 17: Related Work: Benchmarking RS
CompuBench Mobile RenderScript Benchmark
  No source code, offered as an app on Google Play
    Cannot port to other languages
    Not suitable to conduct deep analysis
O2Render [1]: OpenCL to RenderScript translator
  Reuse legacy OpenCL code
  Achieved comparable performance for some simple applications
  Not available to public :(
[1] C. Yang et al. “O2render: An OpenCL-to-RenderScript translator for porting across various GPUs or CPUs,” In Embedded Systems for Real-time Multimedia (ESTIMedia), 2012 IEEE 10th Symposium on, pages 67–74. IEEE, 2012.
Source: https://compubench.com/result.jsp
Notes: O2Render is not offered to public

## Slide 18: Schedule (Phase 0 & 1)

## Slide 19: Schedule (Phase 2 & 3)

## Slide 20: Backup

## Slide 21: Related Work: OpenCL (cont’)
OpenCL vs. OpenMP for multi-core CPUs [1]
  Picked three OpenCL’s worse performing apps
  After tuning the apps -> OpenCL outperformed or similar to OpenMP in 80% test cases
OpenCL performance portability [2, 3]
  [2] <12% performance loss across platforms (Intel Xeon Phi, NVIDIA K20C and AMD 7970 GPU)
  [3] OpenCL is more optimized for GPUs than for CPUs
[1] J. Shen, J. Fang, H. Sips, and A. L. Varbanescu. Performance gaps between openmp and opencl for multi-core cpus. In Parallel Processing Workshops (ICPPW), 2012 41st International Conference on, pages 116–125. IEEE, 2012.
[2] R. Dolbeau, F. Bodin, and G. C. de Verdiere. One opencl to rule them all? In Multi-/Many-core Computing Systems (MuCoCoS), 2013 IEEE 6th International Workshop on, pages 1–6. IEEE, 2013.
[3] K. Komatsu, K. Sato, Y. Arai, K. Koyama, H. Takizawa, and H. Kobayashi. Evaluating performance and portability of opencl programs. In The fifth international workshop on automatic performance tuning, 2010.